## Slide 1: TSim Working Notes
Michael Stanley
Last revised: 8 September 2015

## Slide 2: Project Goals
Create a reproducible methodology for generating stimulus data sets plus expected response for algorithm verification
Tactical Approach
  Inspired by published paper on IMUSim:
  Native Matlab implementation (therefore easy to replicate the environment)
  Create idealized trajectory and orientation construction tools
  Add environmental models
  (3) & (4) feed idealized sensor clusters
  Layer sensor error sources on top of (5)
  Use resulting data for algorithm development & characterization
  Later expand to include import of video motion capture data sets

## Slide 3: Top Level Class Hierarchy
Abstract Trajectory
Position Trajectory
Attitude Trajectory
Composite Trajectory
sinusoid
square wave
triangle wave
Optional “standard” waveforms
Interpolation methods include:
None
Linear
Cubic spline
Slerp (spherical linear interpolation)
Low Pass Filter
Combinations of the above
Position Trajectory models changes in X/Y/Z position Attitude Trajectory models changes in orientation (internally modeled via quaternions)

## Slide 4: Overall Trajectory Construction
At most one of these three paths is active for any one trajectory.
Alternately, P, V or A could be loaded directly
P = Position
V = Velocity
A = Acceleration
RAWPT = piece-wise linear description
integration
integration
derivative
derivative
interpolation /
re-sampling
optional low pass filter
optional sinusoid or other std waveforms
O = Position
AV = Angular Velocity
AA = Angular Acceleration
RAWAT = piece-wise linear description
integration
integration
derivative
derivative
interpolation /
re-sampling
optional low pass filter
At most one of these three paths is active for any one trajectory.
Alternately, O, AV or AA could be loaded directly
optional sinusoid or other std waveforms
Position Trajectory
Attitude Trajectory
Composite Trajectory

## Slide 5: Class Hierarchy continued…
Composite Trajectory
environment
Ideal Sensor Pod
1-axis sensor model
3-axis sensor model
Physical Sensor Pod
Sensor
Fusion

## Slide 6: Environmental Model
Includes:
Frame of Reference
gravity vector (assumed independent of position)
magnetic vector as constant vector or Matlab function
  [ MV ] = f( time, position, temperature)
temperature as constant or a Matlab function
  [ T ] = f( time, position )
air pressure value as constant or a Matlab function
  [ P ] = f( time, position, temperature, altitude)
  default variant is based on standard NASA equations and is independent of time
  Need altitude above sea level at vertical = 0.
  could be based on full 3D model (not likely)

## Slide 7: NASA Standard Atmosphere
C is computed from g0, M0, R* and L
P = P0(T/(T+LH))C
C
Variable | Value | Units
L | -6.50E-03 | K/M
R* | 8.31E+03 | N*m/(kmol*K)
g0 | 9.80665 | m / s2
P0 | 101325 | Pa = N/m2
T | 288.15 | K
M0 | 28.9644 | kg/kmol
C | -5.25588E+00 | 0.1902632
From “U.S. Standard Atmosphere, 1976” , NASA
function [ P ] = standard_air_pressure( position, temperature, time )
% Calculate pressure based on standard equations from NASA:
% "U.S. Standard Atmosphere, 1976".
% Position is of form [X; Y; Z] in meters.
% Temperature is in Celcius
% Time is not used by this version of the function, but is a required
% parameter for the template.
K_to_Celcius = 273.15; % difference between degrees kelvin and Celcius
T = temperature + K_to_Celcius;
H = position(3);
P0 = 101325; % Pascals
L = -6.5e-3; % K/M
C = -5.25588; % C is a precalculated value for the fixed exponential value found in the NASA
% equation. It is calculated as [g0'M0/R*Lm,b]
P = P0*(T/(T+L*H))^C;
end

## Slide 8
function [ t ] = traj9( input_args )
% Create trajectory based on linear interpolation followed by low pass
% filter.
close all;
clc;
LabelPts=1;
initOR = [1; 0; 0; 0]; % initial rotation = none
r = 2*pi();
d=20;
% X Y Z
Adata = [0.0, 0.0, 0.0;
0.0, 0.0, 0.0;
r , 0.0, 0.0;
r , 0.0, 0.0;
0.0, 0.0, 0.0;
0.0, 0.0, 0.0];
Atime = [0; 1; 2; d-2; d-1; d];
Pdata = [0.0, 0.0, 0.0;
0.0, 0.0, 0.0;
1 , 0.0, 0.0;
0.0, 0.0, 0.0;
0.0, 0.0, 0.0;
0.0, 0.0, 0.0;
0.0, 0.0, 0.0];
Ptime = [0; 1; (d/2)+1; d-3; d-2; d-1; d];
% Compute parameters for a low pass filter
% Cutoff frequency=1Hz, sample frequency = 200Hz, 200 taps
% This filter takes several seconds to run, but does a nice job of
% ensuring that our waveforms look reasonable.
% Note that it DOES introduce phase delay (which we don't care about)
[ N, D ] = LPF( 1, 200, 200 );
t = Trajectory('Traj1');
t = t.set_av(initOR, 'linear', Atime, Adata);
t = t.set_position('linear', Ptime, Pdata);
ok = t.precheck(); % Optional
t = t.compute(0.05, 0.005, N, D);
num = sqrt(1/3);
t = t.plot_all(LabelPts, [num; num; num]); % vector chosen for visualizaton purposes only
end
function [ output_args ] = marg_unit_test1( input_args )
Mref = [0; 24.34777; -41.47411];
% Magnetic North Frame of Reference: X=East, Y=North, Z=Up, in microTeslas
P0 = 101325;
env = Env(Env.ENU, [0; 0; 9.80665], Mref, @standard_air_pressure, 25)
t = traj9(); % Pre-defined trajectory
isp = IdealSensorPod(Env.ENU, env, t);
end

## Slide 9: Example: Acceleration Input
% time X Y Z
data = [0, 0.0, 0.0, 0.0;
1, 0.0, 0.0, 0.0;
2, 1.0, 0.0, 0.0;
3, 1.0, 0.0, 0.0;
4, -1.0, 0.0, 0.0;
5, -1.0, 1.0, 0.0;
6, 0.0, 1.0, 0.0;
7, 0.0, -1.0, 0.0;
8, 0.0, -1.0, 1.0;
9, 0.0, 0.0, 1.0;
10, 0.0, 0.0, -1.0;
11, 0.0, 0.0, -1.0;
12, 0.0, 0.0, 0.0;
13, 0.0, 0.0, 0.0 ];
t = t.set_acceleration('spline', data(:,1), data(:,2:4) );
t = t.compute(TimeInc, [], []);
t = t.plot_pt_all(LabelPts);
Yields
via spline fit
Integrates to

## Slide 10: Example: Position Result
2D View
3D View

## Slide 11: Add orientation information
Atime = [0; 1; 2; 11; 12; 13];
Adata = [0, 0, 0; ...
0, 0, 0; ...
1, 0, 0; ...
1, 0, 0; ...
0, 0, 0; ...
0, 0, 0 ];
traj = traj.set_av('linear', Atime, Adata);
...
traj = traj.compute(0.01, 0.005, [], []);
traj.plot_all([1; 1; 1], outputDir);
% Link sensor pod to the environment
% and trajectory
isp = IdealSensorPod(env, traj, ts);
% Plot resultant values
isp.plot_all(outputDir);

## Slide 12: Here’s the entire deck (1 of 2)
function [ output_args ] = isp_example5( input_args )
path(path, '../tool');
outputDir = 'isp_example3_outputs';
close all;
% constant definitions
Mref = [24.3478; 0; +41.4739]; % Magnetic North Frame of Reference: X=East, Y=North, Z=Up, in microTeslas
Gref = [0; 0; -Env.one_g]; % Gravity vector
temperature = 25; % Celcius
Altitude = 400; % value in meters
sample_rate = 10; % sensor sample rate
ts = 1/sample_rate;
% Define the environment
env = Env(Env.NED, Gref, Altitude, Mref, @standard_air_pressure, temperature)
% Define our trajectory
traj = CompositeTrajectory('Constellation');
Atime = [0; 1; 2; 11; 12; 13];
Adata = [0, 0, 0; ...
0, 0, 0; ...
1, 0, 0; ...
1, 0, 0; ...
0, 0, 0; ...
0, 0, 0 ];

## Slide 13: Here’s the entire deck (2 of 2)
traj = traj.set_av('linear', Atime, Adata);
Ptime = 0:13;
Pdata = [0.0, 0.0, 0.0;
0.0, 0.0, 0.0;
1.0, 0.0, 0.0;
1.0, 0.0, 0.0;
-1.0, 0.0, 0.0;
-1.0, 1.0, 0.0;
0.0, 1.0, 0.0;
0.0, -1.0, 0.0;
0.0, -1.0, 1.0;
0.0, 0.0, 1.0;
0.0, 0.0, -1.0;
0.0, 0.0, -1.0;
0.0, 0.0, 0.0;
0.0, 0.0, 0.0 ];
traj = traj.set_acceleration('spline', Ptime, Pdata );
traj = traj.compute(0.01, 0.005, [], []);
traj.plot_all([1; 1; 1], outputDir); % vector chosen for visualizaton purposes only
% Link sensor pod to the environment and trajectory
isp = IdealSensorPod(env, traj, ts);
% Plot resultant values
isp.plot_all(outputDir);
end

## Slide 14: TSIM also supports trajectory animation

## Slide 15: Example: Orientation Input
num = sqrt(0.5);
% Time q0 q1 q2 q3
data = [0, 1.0, 0.0, 0.0, 0.0; % identity
1, num, num, 0.0, 0.0; % 90 about X
2, 0.0, 1.0, 0.0, 0.0; % 180 degrees about X
3, num, -num, 0.0, 0.0; % -90 about X
4, -1.0, 0.0 0.0, 0.0; % back to identity
5, num, 0.0, num, 0.0; % 90 about Y
6, 0.0, 0.0, 1.0, 0.0; % 180 degrees about y
7, num, 0.0, -num, 0.0; % -90 about Y
8, -1.0, 0.0 0.0, 0.0; % back to identity
9, num, 0.0, 0.0, num; % 90 about Z
10, 0.0, 0.0, 0.0, 1.0; % 180 degrees about Z
11, num, 0.0, 0.0, -num; % -90 about Z
12, 1.0, 0.0, 0.0, 0.0
]; % back to starting point

## Slide 16: Example: Orientation
quaternions
angular velocity
angular acceleration

## Slide 17
Want to traverse from q0 to q1 in time t=1
q0•q1 = |q0||q1|cos()
where  is the angle between q0 and q1 (this is the definition of the dot product)
Both q0 and q1have length 1 for this problem, therefore
 = cos-1(q0•q1)
Define θ = t * 
We traverse the angle between q0 and q1 in a linear fashion, interpolating accordingly:
Slerp(q0, q1, t) = q0*sin((1-t) )/sin() + q1*sin((t )/sin()

sin(θ0)
θ
q0 at time 0
q1at time 1
q at time (0<t<1)
Sperical Linear Interpolation
SLERP

## Slide 18: Sensor Features
Trajectory
environment
Ideal Sensor Pod
1-axis sensor model
3-axis sensor model
Specific Sensor Pod
resampling
quantization / change of units
change reference frame
  HAL
  based on sensor alignment
model axis misalignment
temperature effects
Gaussian noise
offset / drift

## Slide 19: Distribution
Released via Open Source License (next page) to the MEMS Industry Group Accelerated Innovation Community GitHub site.
Recommendations for Usage SOPs
  any published algorithm results/status must be based upon centrally controlled “standard releases” of the trajectory and sensor pod classes.
  published results which use custom trajectories must specify (& release for use) those trajectories.
  users are encouraged to submit enhancements for inclusion in future releases
The goal is to encourage development of “standard” test sets and sensor/algorithm parametrics.

## Slide 20: FREESCALE END-USER SOFTWARE LICENSE AGREEMENT
© 2004-2015 Freescale Semiconductor, Inc. All rights reserved.
Redistribution and use in source and binary forms, with or without modification, are permitted provided that the following conditions are met:
Redistributions of source code must retain the above copyright notice, this list of conditions and the following disclaimer.
Redistributions in binary form must reproduce the above copyright notice, this list of conditions and the following disclaimer in the documentation and/or other materials provided with the distribution.
Neither the name of Freescale Semiconductor, Inc. nor the names of its contributors may be used to endorse or promote products derived from this software without specific prior written permission.
THIS SOFTWARE IS PROVIDED BY THE COPYRIGHT HOLDERS AND CONTRIBUTORS "AS IS" AND ANY EXPRESS OR IMPLIED WARRANTIES, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE ARE DISCLAIMED. IN NO EVENT SHALL FREESCALE SEMICONDUCTOR, INC. BE LIABLE FOR ANY DIRECT, INDIRECT, INCIDENTAL, SPECIAL, EXEMPLARY, OR CONSEQUENTIAL DAMAGES (INCLUDING, BUT NOT LIMITED TO, PROCUREMENT OF SUBSTITUTE GOODS OR SERVICES; LOSS OF USE, DATA, OR PROFITS; OR BUSINESS INTERRUPTION) HOWEVER CAUSED AND ON ANY THEORY OF LIABILITY, WHETHER IN CONTRACT, STRICT LIABILITY, OR TORT (INCLUDING NEGLIGENCE OR OTHERWISE) ARISING IN ANY WAY OUT OF THE USE OF THIS SOFTWARE, EVEN IF ADVISED OF THE POSSIBILITY OF SUCH DAMAGE.

## Slide 21: Status
TSIM Base Matlab classes complete
TSIM is fully documented with a 78 page user manual
Pending:
  Physical sensor models correlated to actual devices
  Import of video motion capture databases
TSIM has already been used to verify/debug:
  9 axis Indirect Kalman filter
  9 axis Recursive Least Squares approach

## Slide 22: If you would like to try TSim
You can download the complete Matlab library plus documentation from
  https://github.com/memsindustrygroup/TSim